Simulation #3

ME 565 – Vehicle Dynamics

By: Andres F. Hoyos

Consider a vehicle weighting 3500 lbs, with a pitch moment of inertia of 25000 in-lb-sec^2. Center of gravity equally splits the wheelbase of 8 ft.

l_1 = l_2 = ( 8*12 ) = 96 in.

1. Analytically determine the equivalent suspension stiffness and damping at each corner that will provide a 2 Hz ride frequency:

The desired frequency is 2 Hz which is equal to 4%pi rad/sec.

%omega_des = sqrt( K_a over m_s ) → K_a = %omega_des^2 * m_s → K_a = ( 4%pi )^2*( 3500 over 386.06 ) = 1431.64 lbs/in.

%omega_des = sqrt( K_c over I_y ) → K_c = %omega_des ^ 2 * I_y → K_c = ( 4%pi )^2( 25000 ) = 3947841.75 lbs-in.

Front equivalent suspension stiffness should be 30% less stiff than the rear one.

1.7 K_2 = 1431.64 → K_2 = 1431.64 over 1.7 = 842.14 lbs/in.

K_1 = 0.7*K_2 = 589.50 lbs/in.

2.) Using Olley ride criteria determine appropriate front and rear corner stiffnesses.

The spring center criteria can be applied:

x_sp = -( 0.08)*(2*l ) = -15.36 in.

Ka and Kb can be calculated as follows:

K_a = m_s over {1 - x_sp sqrt {m_s over I_y}} %omega^2 → K_a = ( {3500 over 386.06} over {1 + 15.35 sqrt{(3500/386.06) over (25000)}} )( 2 %pi )^2 = 276.912 lbs/in.

K_c = I_y over {1 - x_sp sqrt{m_s over I_y}} %omega^2 → K_c = ( {25000} over {1 + 15.36 sqrt{(3500 / 386.06) over 25000}} )( 2%pi )^2 = 763604.98 lbs/in.

To determine the front and rear stiffnesses, we propose a front stiffness 30% less stiff than the front one to follow the Olley Ride Criteria.

K_1 + K_2 = 1.7*K_2 = 276.912 lbs/in.

K_1 = 114.02 lbs/in	and	K_2 = 276.91 lbs/in.

3.) Construct a block diagram of the pitch plane vehicle system. Simulate the system response to the vehicle experiencing a time phased 1 in step input.

a